# Retrospeak board revisions
While playing with the SP0256 and retroSpeak I’ve made a few revisions to the PCB

1.0 – First 5V MCP23S17. Found difficulty with powering with 5V with some power supplies. Optional crystal oscillator for fixed frequency.
1.1 – 3.3V MCP23S17
1.2 – Isolated AGND and GND in an attempt to reduce audio noise. Device stable with different PSUs
1.3 – Allow stacking of boards – jumpers to change address of MCP23S17; multiplexed CE1 SPI enable for LTC6903, making it selectable per board. CE1 is OR’ed with a pin on the MCP23S17. A 2N7000 MOSFET is used to increase the logic level. Up to 4 retrospeak boards can be stacked. Ditched fixed crystal.